## Slide 1: Signals and Classifications of Signals
Prof. Dr. Adnan Kavak
Computer Engineering
Kocaeli University
Signals and Systems Fall 2020
This slides are used in EE313 course at the University of Texas at Austin.
They are adopted in this course with Courtesy of Prof. Brian L. Evans
Textbook: Linear Systems and Signals, B.P. Lathi

## Slide 2: Basic Definitions
Audio mixing board
IP camera
Wi-Fi access point
By Scot Duke
SRV statue Austin, TX
Signal
  Carries information
  Patterns of variations in physical quantity
  Function of independent variable (time, etc)
Signal processing signalprocessingsociety.org
  Generation, transformation and extraction of information
  Algorithms with associated architectures and implementations
  Applications related to processing information
System
  Manipulates, changes, records or transmits signals
  Converts a signal into another

## Slide 3: Examples of Signals : 1-ElectroEncephaloGram (EEG) Signal

## Slide 4: Examples of Signals: 2-Stock Market Data

## Slide 5: Examples of Signals: 3-Brain MR

## Slide 6: Classification of Signals
Any signal can be classified as;
  Continuous Time vs. Discrete Time Signals
  Analog vs. Digital Signals
  Deterministic vs. Random Signals
  Periodic vs. Aperiodic Signals
  Even vs. Odd Signals
  Energy vs. Power Signals

## Slide 7: Continuous time vs. Discrete time Signals
Continuous-time signals
  x(t): where t can take any real value
  x(t) may be 0 for range of values of t
  Amplitude values maybe real or complex number
Discrete-time signals
  x[n]: where n  {...-3,-2,-1,0,1,2,3...}
  Unitless sample index n (e.g. day)
  Amplitude values may be real or complex number

## Slide 8: Continuous Time vs. Discrete Time Signals
f0 = 440;
fs = 24*f0;
Ts = 1/fs;
t = 0 : Ts : 4/f0;
x = cos(2*pi*f0*t); plot(t, x);
Continuous-time signals
  MATLAB Code:
Discrete-time signals
MATLAB Code:
sep2016hightemp = [ 96, 92, 92, 93, 94, 95, 96, 95, 95, 93, 93, 93, 94, 92, 94, 95, 96, 98, 99, 99, 96, 94, 93, 97, 88, 73, 80, 89, 86, 83 ];
stem(sep2016hightemp);
title('High Temp. in Austin, TX, Sept. 2016');
xlabel('Day');
ylabel('Degrees F');
ylim( [70 100] );

## Slide 9: Analog vs. Digital Signals
1
-1
At each time value, analog signal amplitude takes real or complex value (a.k.a. continuous-valued)
Digital signal amplitude takes values from a discrete set (a.k.a. discrete-valued)
Analog continuous-time signal
Digital continuous-time signal

## Slide 10: Example

## Slide 11: Deterministic vs. Random Signals
flipnumber = 1:10;
y = sign(randn(10,1));
stem(flipnumber, y);
Random signals
  Cannot be predicted exactly or described by a formula
  Probability distribution of amplitude values can be defined
  Example: Flipping coin 10 times
  Matlab code: uniform distribution
flip
-1
1
Trial #1
flip
-1
1
Trial #2
Deterministic signals
  Mathematically described, e.g. x(t) = cos(2 p f0 t)

## Slide 12: Periodic vs. Aperiodic Signals
A signal x(t) is periodic if for some positive constant T0
x(t)=x(t+T0) for all t,
Otherwise x(t) is aperiodic.
The smallest value of T0 that satisfies perodicity condition of this equation is the fundamental period of x(t).
Fundamental frequency: f0=1/T0 (unit is Hertz –Hz)

## Slide 13: Even vs. Odd Signals
A signal x(t) is said to be even signal if x(t)=x(-t)
A signal x(t) is said to be odd signal if x(t)= - x(-t)
Any signal x(t) can be decomposed into even (xe(t)) and odd xo(t) parts
xe(t)=(1/2)[x(t)+x(-t))]
xo(t)=(1/2)[x(t)-x(-t))]
Even signal
Odd signal

## Slide 14: Energy vs. Power Signals
Size of signal x(t)

## Slide 15: Energy vs. Power Signals
If amplitude of x(t) does not approach zero as time goes to infinity, we should measure power Px of x(t) instead:

## Slide 16: Energy vs. Power Signals

## Slide 17: Sinusoidal Signal
Mathematical form: A cos(w0 t + f)
  A is amplitude/magnitude
  w0 is frequency in rad/s where w0 = 2 p f0 and f0 is in cycles/s or Hz
  f is phase shift in radians
f0 = 440;
fs = 8000;
Ts = 1/fs;
t = 0 : Ts : 3;
x = cos(2*pi*f0*t);
sound(x, fs);
Play As Audio
Smallest period: T = 1 / f0
  Signal x(t) has period T if x(t+T) = x(t) for all t
  Using property cos(x + 2p) = cos(x),
    cos(2p f0 (t + T)) = cos(2p f0 t + 2p f0 T) = cos(2p f0 t)
    when 2p f0 T = 2p or when f0 T = 1 or when T = 1 / f0
  When f0 = 440 Hz, T = 2.27 ms

## Slide 18: Tuning Fork Example A-440 Hz
©2003-2016, JH McClellan & RW Schafer
Estimate Period
Middle plot below gives T ≈ 8.15ms – 5.85ms = 2.3ms
Bottom plot below gives
T ≈ (2 + 2/7) ms = 2.28ms
Estimate Frequency
f0 = 1 / T = 1 / (2.3ms) = 435 Hz
f0 = 1 / T = 1 / (2.28ms) = 438 Hz

## Slide 19: MATLAB Interlude
Matrix Laboratory (MATLAB)
  Released in 1984 to universities
  First toolboxes in control systems and signal processing (1987)
  Semicolon prevents printing result
Scalar variables
Generating vectors
  start : inc : end generate values from start to end at increments of inc
  1 : 0.5 : 3 gives vector [1.0 1.5 2.0 2.5 3.0]
Plot vector x vs. vector t
% Scalar variables
f0 = 440;
fs = 24*f0;
Ts = 1/fs;
% Generate four periods % of time samples
t = 0 : Ts : 4/f0;
% Apply cosine to every
% element of 2 pi f0 t
x = cos(2*pi*f0*t);
plot(t, x);

## Slide 20: MATLAB Interlude
Plot individual samples as stems
Sound card on platform
  Supports specific sampling rates, such as
  8000 Hz for speech and audio
    44100 Hz for CD audio
Playing sound in MATLAB
  sound(vector, rate) will play values of vector at sampling rate and clip values lying outside [-1, 1]
  soundsc(vector, rate) will scale values of vector to be in range [-1, 1] and play scaled values at sampling rate
stem(x);
f0 = 440;
fs = 8000; % rate
Ts = 1/fs;
t = 0 : Ts : 3; % 3 sec
x = cos(2*pi*f0*t);
sound(x, fs);

## Slide 21: Systems
Systems operate on signals to produce new signals or new signal representations
Continuous-time system examples
  y(t) = ½ x(t) + ½ x(t-1)
  y(t) = x2(t)
Discrete-time system examples
  y[n] = ½ x[n] + ½ x[n-1]
  y[n] = x2[n]
T{•}
y(t)
x(t)
T{•}
y[n]
x[n]
Audio, image and communication applications for squaring block
Average of current input and delayed input is a simple filter

## Slide 22: Squaring Block
Applications
  Play AM radio audio transmission
  Displayed pixels on screen undergo ()2.2 nonlinearity
  Increase musical note by one octave on Western scale
Input ‘A’ note at 440 Hz
  x(t) = cos(2 p 440 t)
  y(t) = cos2(2 p 440 t) = ½ (1 + cos(2 (2 p 440 t)) ) = ½ + ½ cos(2 p 880 t)
(•)2
y(t)
x(t)
f0 = 440;
fs = 8000;
Ts = 1/fs;
tmax = 3;
t = 0 : Ts : tmax;
x = cos(2*pi*f0*t);
sound(x, fs);
pause(tmax+1);
y = x .^ 2;
sound(y, fs);
Play As Audio
What frequency does a constant value have?
What frequency does the second term have?
Uses trig identity cos2(q) = ½ + ½ cos(2q)

## Slide 23: Signal Processing Systems
Speech and audio
  Speech compression (cell phones)
  Speech synthesis and recognition
  Audio CD players
  Audio compression: AC3, MPEG 1 layer 3 audio (MP3)
Image and video compression
  Image compression: JPEG, JPEG 2000
  Video CDs: MPEG 1
  DVD, digital cable, HDTV: MPEG 2
  Wireless video: MPEG 4/H.263, MPEG 4 Advanced Video Coding/H.264
Moving Picture Experts Group (MPEG)
Joint Picture Experts Group (JPEG)

## Slide 24: Communication Systems
Digital subscriber lines (DSL)
Cable modems
Cellular phones
  First generation (1G): Advanced Mobile Phone Service
  Second generation (2G): Global System for Mobile (GSM) and Interim Standard-95 (Code Division Multiple Access)
  Third generation (3G): cdma2000, Wideband CDMA
  Fourth generation (4G): Long Term Evolution, Wi-Max
Local area wireless Internet access
  IEEE 802.11a, b, g, n, etc. (“WiFi”)
Digital
Analog